## Slide 1
The Analytical Engine
John Stovin | FSharp Exchange 2019
@johnstovin

## Slide 2
Notes: Around 2010, I stumbled upon Sydney Padua’s 2D Goggles website.
First few episodes of ‘The Thrilling Adventures’, published in 2015.
Pocket universe where L & B use the Analytical Engine to fight crime,
Comics! With Footnotes!
Also a wealth of information on the workings of the Engine
Went to see her talk at Sheffield Library.
Looking for inspiration for an F# project, I thought of an Analytical Engine Simulator

## Slide 3
Notes: The real Charles Babbage (1791 – 1871)
A true polymath
Mathematician, philosopher, inventor and mechanical engineer

## Slide 4
Notes: Note the crank handle
Difference Engine– proof of concept -1819-22
Govt. grant of £1,700 to develop D.E. No. 1 in 1823 (20 digits, 6th order differences)
Designed to calculate & print mathematical tables to eradicate human error
1832 - small working model of part of the mechanism – 6 digits, 2nd order differences
Govt abandoned in1842 after spending £17,000
1846-49 – design for engine No. 2 (31 digits, 7th order differences) fewer parts and faster operation thanks to Analytical Engine

## Slide 5: The Analytical Engine
Notes: Some example code

## Slide 6: Architecture
40- (50-?) digit decimal “word”
1000 word Store
Control flow by punched cards
10s complement for negative values
Notes: Why decimal? So that values could be printed – transcription errors were a big problem
Cards – 4 different readers – synchronisation mechanism not clear
John Walker simplified into a single instruction sequence

## Slide 7: The Mill
Mill performs basic maths operations (+, -, *, /)
2 ingress axes, 1 egress axis
Load operations load ingress axes alternately
2nd load automatically triggers mill operation
Run up lever set if an operation causes an overflow
Notes: Also optional square root unit
This is simplified from Babbage’s designs – I have ignore the primed axes on ingress and egress for example.

## Slide 8
Notes: Started design in 1833
Punched cards for input
Store – 1,000 x 40 (or 50?) digit numbers
Mill – ALU – Add, Subtract, Multiply, Divide, comparison, optional square root
‘Microcode’ architecture – single punched card could trigger a sequence of actions

## Slide 9: Instruction Set
Number Cards
Naaa [+-]nnn… :Store value nnn... at aaa
Operation Cards
+, -, *, /
Variable Cards
Laaa : Load value at aaa into ingress axes
Zaaa : Load value at aaa and set value to zero
Saaa : Save egress axis to address aaa
Notes: John Walker – founder of AutoDesk – has gathered together a lot of Analytical Engine-related material at fourmilab.ch
He devised the instruction set I’m using

## Slide 10: Instruction Set 2
Combinatorial Cards
C[FB][+?]nn
F: forward, B: back, +: always, ?:if run up lever is set
nn: number of instructions to skip
Action Cards
B: Ring bell
H: Halt
P: Print the value on the axis
No character in column1: Comment
Notes: John Walker – founder of AutoDesk – has gathered together a lot of Analytical Engine-related material at fourmilab.ch
He devised the instruction set I’m using
What program should we write to test this out? It’s an FP conference so…

## Slide 11: The Code
Notes: Some example code

## Slide 12: Fibonacci Sequence
N004 30 . No of terms
N000 0 . Constant zero
N005 1 . Constant 1
N001 0 . Previous term
N002 1 . Current term
N003 . Next term
+
L002
P
L001 . curr + prev
S003 . -> next
L002
L000
S001 . curr -> prev
L003
L000
S002 . next -> curr
-
L004
L005
S004 . dec iteration
CF?1 . stop on run up
CB+17 . repeat
B
H
Notes: This is a functional programming conference…
2 columns to make it legible

## Slide 13: The Inner Workings
Notes: John Walker – founder of AutoDesk – has gathered together a lot of Analytical Engine-related material at fourmilab.ch
He devised the instruction set I’m using

## Slide 14: Type Definitions
type Wheel =
| Pos0 | Pos1 | Pos2 | Pos3
| Pos4 | Pos5 | Pos6 | Pos7
| Pos8 | Pos9
type Stack = {
wheels: Wheel list
negative : bool }
Notes: To make this interesting, were not going to use built-in integer maths

## Slide 15: Wheel
module Wheel
open Types
let values = [Pos0;Pos1;Pos2;Pos3;Pos4;Pos5;Pos6;Pos7;Pos8;Pos9]
let indexOf wheel =
values |> List.findIndex (fun v -> v = wheel)
let valueAt index =
values.[index % values.Length]
let inc wheel = valueAt (indexOf wheel + 1)
let dec wheel = valueAt (indexOf wheel - 1)

## Slide 16: (Half) Addition
let add wheel1 wheel2 =
let mutable carry = false
let mutable result = wheel1
let mutable addor = wheel2
while addor <> Pos0 do
addor <- dec addor
result <- inc result
carry <- carry || result = Pos0
(result, carry)
Notes: A binary half-adder takes 2 binary values and provides a result and a carry value – similar for decimal
In the Analytical Engine, only stacks in the mill would have had the ability to carry from one wheel to the next.

## Slide 17: Negative Values
let complements = values |> List.rev
let withComplements = List.zip values complements
let complement wheel =
withComplements
|> List.find (fun w -> fst w = wheel) |> snd
Notes: 2s complement – invert (subtract from 1) each digit then add 1
10s complement – subtract each digit from 9 then add 1
Can also find complement by reading the integer sequence in reverse

## Slide 18: Negate the Stack
let carryUp (carry : bool) (wheel: Wheel) =
((if carry then wheel |> Wheel.inc else wheel),
(wheel = Pos9 && carry))
let add1 wheels =
wheels |> List.mapFold carryUp true |> fst
let complement wheels =
wheels |> List.map Wheel.complement |> add1
let negate stack =
{ wheels = stack.wheels |> complement
negative = not stack.negative }
Notes: Mapfold takes a mapping function, an initial state and a list, applies the fn to each element an returns a tuple of result list and final state

## Slide 19: Full Adder
let add (ingress : Stack list) =
let carryUp carryIn (wheel, carryThrough) =
let wheel' = if carryIn then Wheel.inc wheel else wheel
let carryOut = (wheel = Pos9 && carryIn) || carryThrough
(wheel', carryOut)
let wheels, carry =
List.zip ingress.[0].wheels ingress.[1].wheels
|> List.map (fun (w1, w2) -> Wheel.add w1 w2)
|> List.mapFold carryUp false
let negative =
ingress.[0].negative <> ingress.[1].negative <> carry
let runUp = ingress.[0].negative <> negative
({ wheels = wheels; negative = negative }, runUp )
Notes: This is in the Mill module, so has access to the 2 ingress axes
<> is used as an XOR here

## Slide 20: The Demo
Notes: John Walker – founder of AutoDesk – has gathered together a lot of Analytical Engine-related material at fourmilab.ch
He devised the instruction set I’m using

## Slide 21: Still To Do
Primed ingress and egress axes
Multiplication
Division
Square Roots?
Control Console
Run at realistic speeds
Notes: Primed axes store overflow or modulus values
Multiplication and division requires shift up and down operations, and repeated addition/subtraction
Square roots by Newton-Raphson approximation
Console to allow single stepping and inspection of all values, maybe tracing
Babbage estimated that the engine should be capable of performing a single 40-digit add operation in 19 seconds.
Clever ‘scheduling’ would allow subsequent adds to take around 3 seconds
Multiplying 20 digits by 40 digits would take around 2 minutes – simple step and add would be nearer 8 minutes

## Slide 22: ‘Missing’ Features
Simpler program structure
  (single card sequence)
More branching options
Indexed addressing
Memory -> memory transfers
Notes: If the Engine had been used in anger, users would probably soon ask for more features, including
Now you know how to build an Analytical Engine, so it’s time to…

## Slide 23
Many thanks to Sydney Padua for the use of her amazing illustrations
2DGoggles: http://sydneypadua.com/2dgoggles/
The Thrilling Adventures of Lovelace & Babbage (Particular Books, 2015)
Fourmilab: http://www.fourmilab.ch/babbage/
Code and slides: https://github.com/JohnStov/AnalyticalEngine
Credits & References
Notes: Lots of other Babbage & Analytical Engine resources around the web
Sydney Padua has become a minor Babbage scholar in her own right
There is a class 60 locomotive (No 54) named ‘Charles Babbage’
Babbage briefly worked for the Liverpool & Manchester Railway Company, and invented the locomotive ‘pilot’ designed to prevent stray items on the track from interfering with the locomotive.